## Slide 1
Forecasting Car Crashes on Urban 2-Lane Roads in East Baton Rouge Parish
Michael Allen¹ and Thanos Gentimis2
¹Graduate, Louisiana State University and ²Assistant Professor, Louisiana State University
Motivation
Analysis and Forecast Graphs
Data Analysis
Data
Results
The dataset utilized in this study is sourced from the LSU CARTS statewide crash database.
In selecting the data, a balance was maintained between specificity and quantity. The data needed to be specific enough to provide meaningful insights but not so specific that the counts became too small, which would negatively impact model accuracy.
The study utilizes weekly crash counts from 2018 to 2023 for urban two-lane roads in East Baton Rouge Parish.
Additional engineered features considered include COVID-19 lockdowns, LSU football home games, major holidays relevant to East Baton Rouge Parish, and the presence of ice on roadways.
The data was prepared and analyzed to evaluate its potential for forecasting. Three response variables were tested: raw crash counts and two different denoised count variables.
Multiple model types incorporating various combinations of variables were fitted for each response variable. These included ARIMA, TSLM, and neural network models, along with baseline models such as naïve, seasonal naïve, and drift models.
Each model for every response variable was also fitted using varying train-test split proportions. The test set size was incrementally increased from 5% to 30% in 5% intervals. The root mean square error (RMSE) and residuals for each model were captured and analyzed.
Overall, the ARIMA model containing all the variables performed the best in terms of RMSE and residual analysis.
Many of the denoised models had much lower RMSEs but their residuals had invalidating patterns to them.
References
Centers for Disease Control and Prevention, National Center for Health Statistics. National Vital Statistics System, Mortality 2018-2022 on CDC WONDER Online Database, released in 2024. Accessed at wonder.cdc.gov
Center for Analytics and Research in Transportation Safety (CARTS) Louisiana State University.
Hyndman, R.J., & Athanasopoulos, G. (2021) Forecasting: principles and practice, 3rd edition, OTexts: Melbourne, Australia. OTexts.com/fpp3. Accessed on December 10, 2024.
Car crashes are one of the leading causes of deaths and severe injuries in the United States, resulting in >40,000 deaths in 2022 alone.
Having more accurate knowledge of when crashes may occur will help traffic safety experts more directly address crash patterns.
Figure 3: Weekly Crash Count (grey) and Moving Averages using various window sizes. Note the large drop in early 2020. This is due to Covid-19 lockdowns and is one of the things addressed by the binary exogenous variables.
Figure 4: Classical Additive Decomposition of the CrashCount variable. Note the plateau with double spike pattern that recurs.
Figure 5: Plot showing performance, via RMSE, of models at different Train-Test Split levels. Neural Nets were excluded from the final output due to long computation times without benefit.
Figure 2: Forecast of the ARIMA model with all exogenous variables plus trend and season component predictors at the 20% Train-Test Split level. 80%, 90%, and 95% Confidence Regions shown.
Figure 1: Autocorrelation Function (ACF) for the Crash Count variable.
Objectives
This study aims to compare various models for reliably and accurately forecasting car crashes on urban two-lane roads in East Baton Rouge Parish.
Link to the code and resources for this project.